# 78EKG-2                                                                                Sr. No. 5

# EXAMINATION OF MARINE ENGINEER OFFICER

# ENGINEERING KNOWLEDGE

(GENERAL)

### CLASS II

(Time allowed - 3 hours)

Total Marks 100

INDIA                                                                          Morning Paper

N.B. -        (1) Attempt SIX questions ONLY.

(2) All questions carry equal marks.

(3) Marks for each part question are shown in brackets.

(4) Neatness in handwriting and clarity in expression carries weightage

- You have been appointed as the Second Engineer of a ship which has a transverse bow thruster unit using a controllable pitch propeller. A specific problem has arisen in the power developed by the bow thruster. There is possibly a need to change the prime mover for the controllable pitch propeller. Draft a letter to the owners explaining the technicalities of selection of a prime mover giving adequate reasons for selection of a thrust unit delivering a relatively low pressure head with high volume output rather than a high pressure head with low volume output.                                        (16)

- The vessel on which you are serving has been subjected to port state control. The procedures for port state control apply to ships which come under the provision of certain international convention and protocols. State those conventions and protocols and specifically point out the areas covered by certification, which are issued under these conventions and protocols.																		    (16)

- Sketch a sealing arrangement for an oil lubricated stern tube; and –															               (6)

- Identify the common forms of seal failure.                                                                                    (4)

- State how oil loss due to seal failure can be restricted whilst on passage?                                    (3)

- What are the materials used for sealing rings and propeller shaft liner?                                       (3)

- A shaft system is excessively misaligned so as to cause serious bending of the shaft. State what effect this could have on: -												                                                                                                 (8)

- Shaft coupling bolts.

- Shaft bearing

Having identified the effects in (a) and (b) state which one of them would cause more reason for concern and why?                                                                                                                                 (8)

- Reverse Osmosis is the modem alternative for shipboard production of drinking water:

- Describe, using simple diagrams where necessary, the principles of:                                          (10)

(i) Osmosis  (ii) Reverse Osmosis

- What maintenance is essential to ensure satisfactory functioning of such a system?                   (6)

- (a) Sketch a nozzle/flapper device used for the generation of pneumatic signal, labeling the component parts.                                                                                                                                 (8)

- Describe the operation of the device in Q. 6(a)                                                                            (4)

- State a particular equipment on board ships which uses your device explaining the functioning of that equipment.                                                                                                                             (4)

- Using simple sketches to illustrate water flow or reaction, describe how a rudder can steer a vessel or act as a velocity retarder. With reference to arresting the headway of very large vessels explain:   (16)

- Why full astern power is usually less than full ahead power;

- Why rudder adapted to act as retarders have not been successful;

- The part that a transverse thrust unit could play in reducing stopping distance.

8.  Short cycling of a refrigeration compressor refers to one or a combination of the following:

- Leakage of solenoid valve

- Need to charge gas

- Abrupt change of speed

- Does not develop adequate discharge pressure

State the correct answer giving specific reasons, why the other points cannot be considered as reasons for short cycling?                                                                                                               (16)

- The emergency bilge suction valve is typically used for one or combination of the following:

- to inject cleaning additives when the bilges are extremely dirty

- when the main condenser becomes fouled, in order to provide additional cooling water circulation

- to connect the rose box to the independent bilge suction

- if the bilges become flooded and they can not be emptied by any other means

State the correct answer giving specific reasons, why the emergency bilge suction and not any other bilge suction valve is used for the purpose.                                                                                     (16)

----------------------------------------X----------------------------------