# 95MEKM-2

# Sr. No. 2

# EXAMINATION OF MARINE ENGINEER OFFICER

# Function: Marine Engineering at Management Level

# MARINE ENGINEERING KNOWLEDGE

(MOTOR)

### CLASS II

(Time allowed - 3 hours)

INDIA (2001)			                                       Morning Paper	                       Total Marks  100

N.B. -    (1) Attempt SIX Questions Only.

(2) All Questions carry equal  marks.

(3) Neatness in handwriting and clarity in expression carries weightage

- Describe, as Chief Engineer, the procedure you would adopt to ensure efficient operation of exhaust gas turbo-chargers and explain the possible consequences if proper attention is not afforded to this equipment.

- Sketch and describe a steam raising plant which utilises exhaust gas energy and which can replace an engine silencer. What would be the effect of lack of water in this plant?

- In the case of a main propulsion engine explain the indications and possible effects which might be expected from:

- insufficient bearing clearance,

- excessive bearing clearance and

- crankshaft misalignment

State the recommended bearing clearances for the bottom end, top end and main bearings of your last motor vessel.

- Explain the possible reasons for and describe your subsequent actions in the case of the following changes in service of Diesel engine lubricating oil:

- flash point increase,

- viscosity increase.

- Discuss the probable causes of the following:

- explosions in:

(i) crankcases

(ii) starting air lines,

- scavenge fires.

- Consideration has been given to running Diesel machinery untended at night. Describe the modifications and additional apparatus, which would be necessary before this could be achieved with reasonable safety.

- Enumerate the factors, which determine the temperature and pressure in a compression ignition engine at the instant of fuel injection. Show, on typical indicator diagrams, the effects of incorrect values and explain the possible consequences on engine operation.

- Discuss critically the following alternative types of main propelling machinery for installation in proposed new vessels:

- Opposed piston.

- Four-stroke single acting.

- Two-stroke single acting.

- Gas turbines.

- Sketch and describe the construction of a cylinder air-starting valve. Explain fully how it is operated and draw a timing diagram, mentioning the type of engine and number of cylinders to which it applies.

What are the dangers of a valve leaking or partially sticking, open and how would this defect be detected when the engine is running?

------------------------------X------------------------------