95MEP-2

Sr. No. 4

EXAMINATION OF MARINE ENGINEER OFFICER

Function:  Maintenance & Repair  at Management Level

MARINE ENGINEERING PRACTICE

M.E.O. Class II

(Time allowed - 3hours)

India (2002)                                                              Morning Paper                 Total Marks  100

N.B. -    (1) Answer SIX Questions Only.

(2) All questions carry equal marks.

(3) Neatness in handwriting and clarity in expression carries weightage

- Suggest a procedure (in about 200 words) to the Chief Engineer, on how you propose to ensure that the engine room exhaust fans are maintained and operated correctly.

- Write short notes on the following:

  - Measures to stop exhaust gas  leakage in  the engine room

  - Measures to stop oil leakages in the engine room.

- A squealing sound occurring from within an operating reciprocating air compressor is an indication of __________.

  - compressor overload

  - motor overload

  - tight compressor bearings

  - badly leaking unloaders

Give Reasoned Explanation to Your Answer

- How does short cycling of a refrigeration compressor take place and what are the indications. How can such a condition be avoided.

- What is the emergency bilge suction valve typically used for? State the maintenance required to keep it operational.

- What all would be the causes, and what checks would you carry out, if the intercooler relief valve lifts while an air compressor is operating under load.

- Why are removable sleeves installed on centrifugal pump shafts?

- They make it easier to replace the pump shaft packing.

- They can be economically replaced as they wear out.

- They can be removed when it is necessary to lighten the weight of the pump.

- They increase the strength of the shaft.

Discuss each one of the points  and state why you would prefer to select or reject any one of the them

- If a reciprocating air compressor has a knock occurring in frequency with its operating RPM, the cause is probably ____________.

- misalignment or worn main bearings

- insufficient cylinder lubrication

- defective or poorly fitted valves

- all of the above

Discuss each one of the points  and state why you would prefer to select or reject any one of the them

- A good quality oil used in main propulsion engine lubrication systems should be _____________.

- free from all chemical additives

- quickly chemically oxidized

- resistant to permanent emulsification

- readily saponified with water

Discuss each one of the points  and state why you would prefer to select or reject any one of the them

- In a compression type grease cup, the lubricant is forced into the bearing by ____________.

- gravity flow

- spring force

- a pressure gun

- a jerk fitting

Discuss each one of the points  and state why you would prefer to select or reject any one of the them

-----------------------------X-------------------------

95MEP-2

Sr. No. 4

EXAMINATION OF MARINE ENGINEER OFFICER

Function:  Maintenance & Repair  at Management Level

MARINE ENGINEERING PRACTICE

M.E.O. Class II

(Time allowed - 3hours)

India (2002)                                                              Morning Paper                 Total Marks  100

N.B. -    (1) Answer SIX Questions Only.

(2) All questions carry equal marks.

(3) Neatness in handwriting and clarity in expression carries weightage

# Answers

Answer for Question No. 3             Correct Answer : C

Answer for Question No. 7                  Correct Answer : B

Answer for Question No. 8                  Correct Answer : A

Answer for Question No. 9                  Correct Answer : C

Answer for Question No. 10                Correct Answer : B