###### 95MEP-2

Sr. No. 5

EXAMINATION OF MARINE ENGINEER OFFICER

Function:  Maintenance & Repair  at Management Level

MARINE ENGINEERING PRACTICE

M.E.O. Class II

(Time allowed - 3hours)

India (2002)                                                              Morning Paper                 Total Marks  100

N.B. -    (1) Answer SIX Questions Only.

(2) All questions carry equal marks.

(3) Neatness in handwriting and clarity in expression carries weightage

- A number of main engine cylinder covers have been subject to cracking during the proceeding four months. Write a brief report to the Engineering Superintendent

- Explaining possible causes

- Steps taken to reduce the possibility of cylinder cover cracking in future.

- Describe the maintenance/ inspection of the following items of an a.c motor control gear

(a)   Enclosure

- (b)   Contacts

(c )  Connection

- (d)   Over current relays

- With reference to turbo – chargers state how :

- a damage blade may be replaced.

- axial clearance between rotor/ casing is measured and adjusted.

- the performance may be assessed

- Following are some of the defects which may occur to the combustion chamber of an auxiliary boiler

- Deformation

- Wastage

- Cracks

Discuss causes and suggest repairs to rectify the defects.

- Under continuous survey of machinery programme of a classification society bottom end

bearing of a large slow speed engine is due for survey.

- Describe the procedure to open up the above item and ready it for survey.

- List the precautions to be taken.

- What tests are to carried out on completion of survey and re assembly.

- Thrust block fitted to a reversible engine is found to be running hot.

(a)    List the causes.

- How the clearance between collar and pads is measured and adjusted.

- Ahead pads have run out and no spares are available on board. What steps will you

take to bring the ship to port.

- (a)   Describe the inspection and maintenance of Ex ‘d’ (flameproof ) enclosures for

luminaries installed in hazardous condition.

- List the precautions to be taken while carrying out insulation resistance test of

electrical  equipment located in a hazardous area.

- Performance of a control system has deteriorated due to which controlled condition :

- goes to one or other extreme of its range

- stays at zero

(c)   oscillates

Discuss the causes and steps taken to rectify the faults.

- (a)    As per Regulation 19-2 of chapter V of SOLAS 1974/78 as amended, ships

steering gear shall be checked and tested with in 12 hrs. before departure.

List the items and procedure for their testing.

- Describe emergency steering drill and its periodicity.

--------------------------X-------------------------------