95MEP-2

Sr. No. 5

EXAMINATION OF MARINE ENGINEER OFFICER

Function:  Maintenance & Repair  at Management Level

MARINE ENGINEERING PRACTICE

M.E.O. Class II

(Time allowed - 3hours)

India (2003)                                                    Morning Paper                 Total Marks  100

NB :	(1) Answer SIX  Questions only.

(2) All Questions carry equal marks

(3) Neatness in handwriting and clarity in expression carries weightage

(4) Illustration of an Answer with clear sketches / diagrams carries weightage.

1.      With reference to the provision of a shore electrical supply to a ship:

- Sketch an arrangement for taking A.C. shore supply;

- Describe the method of safely connecting the arrangement sketched in (a) to the shore  supply.

2.      (a)Explain in detail how an in-water survey is carried out.

(b)State the requirements to be fulfilled before an in-water survey is acceptable to the  survey authority.

(c)Construct a list of the items in order of importance that the underwater survey    authority should include.

3.    Accidents regularly occur due to premature  accidental release of CO 2 into machinery spaces. With reference to this, state the procedure or arrangements that  you as Second  Engineer would adopt with respect to the following:

(i) Contractors working on the CO 2 system;

(ii) Understanding between bridge and engine room in the event of fire.

- Give  a detailed note on the following measures with reference to safety , legal aspects and  operational requirements

  - Measures to stop exhaust gas  leakage in  the engine room

  - Measures to stop oil leakages in the engine room.

5.   How does short cycling of a refrigeration compressor take place and what are the    indications. How can such a condition be avoided.

- How can the by-products of oxidation as a result of water contamination of hydraulic oil   be removed. How can such oxidation of oil be minimized.

- What can be the possible causes of a fresh water generator vacuum not reaching the  desired value for optimum operation.

8.     With reference to on-load cleaning of the gas side of main boilers:

- Explain how cleaning is affected in some arrangements where steam jets oppose gas                flow.

- Explain how a distorted long retractable soot blower element may be dealt with and     suggest what may have been the cause.

- State possible objections to employing a system comprised of high frequency sound generators.

9.   Write Short notes on

      - Deoxidation process of boiler feed

      - Safe practices in changing mechanical seals of high pressure pumps

      - Correct method and tools to be used for extracting bearings

-----------------X----------------