95NA-2

Sr. No. 6

EXAMINATION OF MARINE ENGINEER OFFICER

Function:  Controlling the Operation of The Ship & Care for Persons on Board  at Management Level

NAVAL ARCHITECTURE

M.E.O. Class II

(Time allowed - 3hours)

India (2003)                                       		          Afternoon Paper                            Total Marks  100

NB : (1)Answer SIX  Questions :

SECTION -1 :- Answer atleast TWO  Questions

SECTION -2 :- Answer atleast TWO  Questions

(2)All Questions carry equal marks

(3)Neatness in handwriting and clarity in expression carries weightage

(4) Illustration of an Answer with clear sketches / diagrams carries weightage.

# Section - 1

- With reference to dry docking, define the responsibilities of the chief engineer:

- Prior to docking;

- Whilst the vessel is in dry dock;

- Prior to flooding and leaving the dock.

- State FOUR sources of excitation that may induce vibration into the main hull girder.

- Suggest methods for reducing the vibration levels induced by EACH of the exciting forces in.

- Show, with the aid of diagrammatic sketches, how a large ship is supported in dry dock. Indicate the strains that are imposed on a ship resting on the blocks. Detail the precautions that should be taken when refloating the ship in a dry dock.

- With reference to ship’s rudder state:-

- Why a breached hollow rudder can add to fuel costs?

- Why excessive pintle clearance should not be tolerated?

- Why fitted bolts are used in connecting upper and lower stocks?

- Keeping the draft of a ship at, or below the load line mark, insures the unit will have adequate          ______________.

- reserve ballast

- reserve buoyancy

- lightweight displacement

- critical motion

Give reasoned Explanation to your Answer

Section – 2

- A ship of 5080 tonne displacement and KM = 6.4m is inclined in sea water by moving a mass of 5.0 tonne transversely through a distance of 14.6m. This caused a pendulum 6.lm long to be deflected 10.2cm. During the experiment a double bottom tank, 7.3m long ( 9.lm broad ( 1.22 m deep, contained sea water to a depth of 0.61 m. Find the KG of the light ship if the only deadweight was the water in the tank.

- The end bulkhead of an oil fuel bunker is in the form of a rectangle 10 m wide and 12 m high. Find the total load and the position of the centre of pressure relative to the top of the bulkhead if the tank is filled with oil of specific gravity 0.9: (a) to the top edge  (b) with 3 m head to the top edge.

- A ship 125m long displaces 12000 tonne. When a mass of 100 tonne is moved 75m from forward to aft there is a change in trim of 65 cm by the stern. Calculate:

- MCTI cm

- The longitudinal metacentric height

- The distance moved by the centre of gravity of the ship.

- A ship of 15000 tonne displacement has an Admiralty Coefficient, based on shaft power, of 420. The mechanical efficiency of the machinery is 83%, shaft losses 6%, propeller efficiency 65% and QPC 0.71. At a particular speed the thrust power is 2550kW.

Calculate:

- indicated power,

- effective power,

- ship speed.

- An oil tanker has LBP 142m, beam 18.8m and draught 8m. It displaces 17000 tonne in seawater of 1.025 t/m3. The face pitch ratio of the propeller is 0.673 and the diameter 4.8m. The results of the speed trial show that the true slip may be regarded as constant over a range of speeds of 9 to 12 knots and is 35%. The wake fraction may be calculated from the equation:

w = 0.5Cb – 0.05

If the vessel uses 20 tonne of fuel per day at 12 knots, and the consumption varies as (speed) 3, find the consumption per day at 100 rev/min.

---------------------------X-------------------

95NA-2

Sr. No. 6

EXAMINATION OF MARINE ENGINEER OFFICER

Function:  Controlling the Operation of The Ship & Care for Persons on Board  at Management Level

NAVAL ARCHITECTURE

M.E.O. Class II

(Time allowed - 3hours)

India (2003)                                       		          Afternoon Paper                            Total Marks  100

NB : (1)Answer SIX  Questions :

SECTION -1 :- Answer atleast TWO  Questions

SECTION -2 :- Answer atleast TWO  Questions

(2)All Questions carry equal marks

(3)Neatness in handwriting and clarity in expression carries weightage

(4) Illustration of an Answer with clear sketches / diagrams carries weightage.

Answers

## Answer for Question No. 5   Correct Answer : B

Answer for Question No. 6

5.485m